## Slide 1: Investigating remote sensing datasets to model natural flood management options in the Ba River catchment, Viti Levu Eleanor Earl, PhD Candidate at UNSW
PGRSC
November 2023
Supervisors:
A/Prof Fiona Johnson
Prof Lucy Marshall
Prof David Sanderson

## Slide 2
Acknowledgements
We’d like to acknowledge the support of many individuals and organisations who have made this research possible:
Ms Swastika Prasad and Mr Bipen Prakash at Fiji Metrological Service
Mr Vilimone Raqona at Fiji Ministry of Lands and Minerals
Mr Ravuama Nagatalevu (PA Ba), Mr Sivendra Michael (UNDP) and Mr Joshua Elisha (Rise Beyond the Reef)
Dr John Duncan at the University of Western Australia, Prof Andreas Neef at the University of Auckland, Dr Floris van Ogtrop, Dr Kevin Davies at the University of Sydney,
Ms Jacqui Reid, Mr Nicholas Metherall and Mr Amit Singh from SPC, Fiji.
The Vinaka Family in Ba

## Slide 3
What is the impact of flooding?
In the past 20 years floods have affected 570,000+ lives in the Pacific Islands1
(1) EM-DAT and CRED/UCLouvain (2023). Emergency Events Database. Brussels, Belgium, The Centre for Research on the Epidemiology of Disasters (CRED).

## Slide 4
Why use natural flood management to improve resilience?
Sketch by E. Earl adapted from Reed, B (2007) Shifting from ‘sustainability’ to regeneration and CIRIA SUDS Manual (2015)
Tailored to the local ecology

## Slide 5
Natural Flood Management Tunnel Vision
Sketch by E. Earl adapted from Konietzko, J. (2007) Moving-beyond-carbon tunnel vision with a sustainability data strategy with ideas from Raworth, K. (2017) Doughnut Economics: Seven Ways to Think Like a 21st-Century Economist and the IUCN Global Standard for Nature-based Solutions (2021)
Natural Flood Management
Nature-based approaches
Air pollution
Biodiversity loss
Land & resources
Freshwater withdrawals
Nitrogen & phosphorus loading
Chemical pollution
Ocean acidification
Ozone depletion
Social inequality
Energy
Education
Health
Livelihoods
Infrastructure
Food
Peace & justice
Governance & policy
Climate change

## Slide 6
  What available data sets can be used and can NFM be spatially optimised?
Research question…

## Slide 7
Can NFM be spatially optimised using free software?
HEC-RAS
Call command used in shell script to run python code on UNSW HPCs
Python code identifies which land use areas are in each grid cell
Python code iteratively changes land use parameters in each grid cell
Python
Software can be downloaded for free (but not open source)
Since 2016 2D Unsteady analysis
Since 2021 hydrology and hydraulics can now be modelled seamlessly
Linux version compatible with High Performance Computers (HPCs)
ArcGIS/GIS
Processing geospatial datasets for input in to the ‘seed’ HEC-RAS model
Choosing model grid

## Slide 8
Abstraction Ratio
Mannings N
Curve Number
Impermeable Area
How do NFM mechanisms reduce flooding?
Reduce runoff
Infiltrate
Store
Slow
Natural Flood Management
Mechanisms
Model Parameters

## Slide 9
Why Ba?
17 Feb 2023
3 Jan 2023
7 Mar 2023
Recent newspaper articles from Ba, Fiji

## Slide 10
What were the main remote sensing data inputs?
Lower catchment 1m LiDAR (Neef et al. 2020) remaining areas 30m Copernicus DEM GLO30 (2010 to 2014)
Topography
Neef, A., Boruff, B., Bruce, E., Ngin, C., Pauli, N., Davies, K., Van Ogtrop, F., Varea, R., Weber, E. (2020). Climate change adaptation in disaster-prone communities in Cambodia and Fiji. Science Bulletin, 10(1), 67-75.
Copernicus WorldDEM-30 © DLR e.V. 2010-2014 and © Airbus Defence and Space GmbH 2014-2018 provided under COPERNICUS by the European Union and ESA; all rights reserved
NASA JPL (2013). NASA Shuttle Radar Topography Mission Global 1 arc second [Data set]. NASA EOSDIS Land Processes DAAC. Accessed 2020-12-03 from https://doi.org/10.5067/MEaSUREs/SRTM/SRTMGL1.003
Davies et al. 2021. A Dynamic, Cloud-based LULC Mapping Methodology Using Sentinel-2 to Support Climate-Smart Landscape Management in Vulnerable Fijian Communities, Environmental Science.
Land use
Land use (Davies et al. 2021)
ML model using Sentinel-2 10m land use data

## Slide 11
Why did I choose Copernicus DEM GLO30?
Lower catchment 1m LiDAR (Neef et al. 2020) remaining areas 30m Copernicus DEM GLO30 (2010 to 2014)
Topography
Neef, A., Boruff, B., Bruce, E., Ngin, C., Pauli, N., Davies, K., Van Ogtrop, F., Varea, R., Weber, E. (2020). Climate change adaptation in disaster-prone communities in Cambodia and Fiji. Science Bulletin, 10(1), 67-75.
Copernicus WorldDEM-30 © DLR e.V. 2010-2014 and © Airbus Defence and Space GmbH 2014-2018 provided under COPERNICUS by the European Union and ESA; all rights reserved
NASA JPL (2013). NASA Shuttle Radar Topography Mission Global 1 arc second [Data set]. NASA EOSDIS Land Processes DAAC. Accessed 2020-12-03 from https://doi.org/10.5067/MEaSUREs/SRTM/SRTMGL1.003
GLO-30
Flattening of water bodies and consistent river flow, leading to smoother river channel profile
Values at boundary closely fit with LiDAR data
30m SRTM
Rough river channel profile
Values at boundary poorly fit with LiDAR data

## Slide 12
What were the main remote sensing data inputs?
Land use
Land use (Davies et al. 2021)
ML model using Sentinel-2 10m land use data
Land Cover type | Percentage land cover (%) | 
 | Davis et al. 2021 | ESA WorldCover 10 m 2021 v200
Water | 0.8 | 0.5
Mangrove/ Woody wetland | 0.5 | 0.6
Bare soil | 0.6 | 0.3
Urban | 0.7 | 0.32
Crop | 15.7 | 1.0
Grassland | 34.7 | 34.6
Shrubland | 39.7 | 0
Forest | 7.38 | 63
Zanaga, D., Van De Kerchove, R., De Keersmaecker, W., Souverijns, N., Brockmann, C., Quast, R., Wevers, J., Grosu, A., Paccini, A., Vergnaud, S., Cartus, O., Santoro, M., Fritz, S., Georgieva, I., Lesiv, M., Carter, S., Herold, M., Li, Linlin, Tsendbazar, N.E., Ramoino, F., Arino, O., 2021. ESA WorldCover 10 m 2020 v100. https://doi.org/10.5281/zenodo.5571936
Davies et al. 2021. A Dynamic, Cloud-based LULC Mapping Methodology Using Sentinel-2 to Support Climate-Smart Landscape Management in Vulnerable Fijian Communities, Environmental Science.

## Slide 13
How does land use data impact the model?
ESA WorldCover 10m (Zanaga, D. et al. 2020)
Mannings N Parameter Sensitivity
ML model using Sentinel 10m land use data (Davies et al. 2021)
Mannings N Parameter Sensitivity
JICA 1998. The study on watershed management and flood control for the four major Viti Levu rivers, Final Report, Yachiyo Engineering Co. Ltd.
Zanaga, D., Van De Kerchove, R., De Keersmaecker, W., Souverijns, N., Brockmann, C., Quast, R., Wevers, J., Grosu, A., Paccini, A., Vergnaud, S., Cartus, O., Santoro, M., Fritz, S., Georgieva, I., Lesiv, M., Carter, S., Herold, M., Li, Linlin, Tsendbazar, N.E., Ramoino, F., Arino, O., 2021. ESA WorldCover 10 m 2020 v100. https://doi.org/10.5281/zenodo.5571936
Davies et al. 2021. A Dynamic, Cloud-based LULC Mapping Methodology Using Sentinel-2 to Support Climate-Smart Landscape Management in Vulnerable Fijian Communities, Environmental Science.
PEAK FLOWS HIGHER IN
ML MODEL
AVERAGE PEAK FLOW CLOSER TO EXPECTED VALUE IN ML MODEL
TIME OF CONCENTRATION EARLIER IN ML MODEL

## Slide 14
Can NbS be spatially optimised to reduce flooding?
UPPER CATCHMENT
LOWER
CATCHMENT
C
B
A
Compare NFM changes anywhere across the catchment

## Slide 15
What different scenarios can be modeled?
Scenarios
Rainfall event
Land cover parameters
Flow
Depth
Grid
Location

## Slide 16
Ba Catchment 16km² grid 6hr 2yr AEP
Ba Catchment 16km² grid 24hr 2yr AEP
Can NFM be spatially optimised to reduce flooding?
Values = No relative change
Values = No relative change

## Slide 17
Monitoring and evaluation
Working at macro and micro scales
Key opportunities for the RS/GIS community
Computational demand
RS could improve model inputs

## Slide 18
How could remote sensing improve modelling NFM?
Natural Flood Management
Flow measurements
Biodiversity change
Soil moisture
Sediment transport
Evaporation
DEM
Land use
Transpiration

## Slide 19
Conclusions and gaps for future research
Numerical models could be used more in flood management decision-making in Pacific Islands1
Remote sensing research is needed to reflect these complex systems.
(1) Earl, E. et al., 2023. A critical review of Natural Flood Management application and spatial prioritisation approaches in tropical island catchments, Science of The Total Environment, Volume 878, 2023,doi.org/10.1016/j.scitotenv.2023.162776.
Next steps to trial on a smaller catchment

## Slide 20
Vinaka vaka levu!
Eleanor Earl
e.earl@unsw.edu.au
www.linkedin.com/in/eleanor-earl-32186635
Scientia PhD Scholar
UNSW Water Research Centre
Ba Catchment, Fiji (E. Earl 2022)