## Slide 1: Pacific Islands GIS and Remote Sensing User Conference 2024
THEME: ‘’Sustainable Management of Coastal Areas through remote sensing and GIS’’
Presenter: Johnny Tarry NIMAU
Snr. Monitoring and Evaluation Officer,
PARTneR II Country Liaison,
Vanuatu PGRSC Focal-Point
Department of Climate Change, MOCC, Vanuatu
Notes: Brief introduction on the Theme along with Vanuatu Context and align with the national priorities through the PARTneR II Project

## Slide 2: Hazard Exposure and Losses to Extreme Wave Levels Exacerbated by Climate-induced Sea-Level Rise in Vanuatu Islands Contexts
Johnny Nimau4, Rebecca Welsh1, Ryan Paulik1, Shaun Williams1, Juli Ungaro1, Cyprien Bosserelle1, Rose Pearson1, James Battersby1, Luisa Hosse1, Antonio Espejo2, Tim Beale3, Herve Damlamian2, Litea Biukoto2, Judith Giblin2, Thompson Auri2, Kaliopate Tavola2
1 National Institute of Water and Atmospheric Research Ltd Taihoro Nukurangi, Te Whanganui-a-Tara Wellington 6021, Aotearoa New Zealand
2 The Pacific Community, SPC Geoscience Division, Suva, Fiji
3 Catalyst IT, Ōtautahi Christchurch 8011, Aotearoa New Zealand
4 Climate change and National Disaster Management Office, Ministry of Climate Change and Adaptation, Vanuatu
Notes: Introduction to PARTneR II Project through Funding support from New Zealand –MFAT and Managed by NIWA and SPC in partnership with Vanuatu, Samoa, Cooks Island, Tonga, Tuvalu and RMI.

## Slide 3: PARTneR-2 Project
Aim: Pacific Island Countries are more resilient to the impacts of climate change through risk-informed decision making.
Countries involved: Cook Islands, Republic of Marshall Islands, Samoa, Tonga, Tuvalu, Vanuatu

## Slide 4: Sea Level Rise in Vanuatu
Expected to impact 25% – 50% of people in Vanuatu Islands.
SLR has risen 1.5mm per year in Vanuatu from 1900 to 2008 (almost 10cm).
Coupled with vertical land movement.

## Slide 5: Step 1: Hazard Maps
 | PARTneR-2 Countries
ARI | MHWS, 5, 10, 25, 50, 100, 250
SLR | 0-2m in 10cm increments
Where? | Available on Nexus: https://nexus.pacificdata.org
Luganville, Vanuatu ARI100 from 0 – 2m

## Slide 6: Digital Elevation Models
DEM: A digital representation of bare ground topography with trees, building and other ground cover excluded.
PARTneR-2 Countries
5m cell size. Down-sampled LiDAR and up-sampled FABDEM where LiDAR is not available.
Tanna, Vanuatu Digital Elevation Model

## Slide 7
Digital Elevation Model
Bathtub Model Process
Total Water Levels
National SLR Maps
Port Vila, Vanuatu

## Slide 8: Risk Models
Hazard Information
Exposure Information
Vulnerability Models
Impacts
e.g. Flooding, Coastal Inundation, Wind, SLR, Drought
e.g. Buildings, People, Infrastructure, Crops
Calculate how the hazards impact the exposure layers
Tailored Maps, Tables, Reports, Dashboards

## Slide 9: RiskScape
https://riskscape.org.nz/
Risk decision support tool.
Open-source spatial data processing application used for multi-hazard risk analysis.
Highly customisable from simple exposure models to computationally intensive probabilistic models.

## Slide 10
Port Vila FloodDepth 5 _1.0
Port Vila FloodDepth 10 _0.5
Port Vila FloodDepth 25_0.5
Port Vila FloodDepth 50 _0.5

## Slide 11
Port Vila FloodDepth 100 _0.5
Port Vila FloodDepth 250 _1.5

## Slide 12: RiskScape Platform

## Slide 13: Exposure
The Single-Event Model calculates loss and exposure to a range of different assets e.g. buildings, population, crops, infrastructure, at an individual asset scale and aggregated to region and use type.
Loss
Single-Event Model
Zoomed in to part of Port Vila, Vanuatu - ARI100 with 1.0m SLR
Vanuatu - ARI100 with 1.0m SLR
Chart: Loss by Building Use Type
| Commercial | Educational | Industrial | Infrastructure | Institutional | Other | Out building | Public | Residential | Unknown
Total_Loss | 14476425 | 53912 | 919461 | 579675 | 2327375 | 604089 | 2243020 | 1724743 | 28684720 | 33735852

## Slide 14: Average Annualised Loss
Average Annualised Loss (AAL): Expected loss per year, averaged over many years. It is rough measure of the ‘riskiness’ of a set of exposures.

## Slide 15: Vanuatu GIS Users
National GIS User group
MOCC GIS Users

## Slide 16: Capacity Building- GIS initiatives

## Slide 17
GIS Products developed to inform decision making, Plannings, Preparedness, Response, Recovery
Notes: Challenges encountered: Lack of resources, capacity building, data collection/sharing, and capital to ran the GIS show

## Slide 18: Manaro Volcano Exposure Map
Volcano Hazards and Evacuation Route

## Slide 20: Coastal Rehabilitation: Mitigation and Adaptation Best Practices
Notes: Challenges include a lack of resources, capacity building, data collection/sharing, and Capital to act on the risk-informed information.

## Slide 21
Tangkiu tumas
Contact: johnie@vanuatu.gov.vu